## Slide 1
Reference: Title Page & Abstract
INVys: Indoor Navigation System for Persons with Visual Impairment Using RGB-D Camera
Widyawan, Muhammad Risqi Saputra, Paulus Insap Santosa
Universitas Gadjah Mada (Yogyakarta) and Monash University Indonesia
JNTETI, Vol. 12 No. 4, November 2023
1 / 35

## Slide 2
Reference: Abstract
System Overview
Problem: indoor navigation for persons with visual impairment
Solution: INVys system using an RGB-D camera
Micronavigation: depth information; novel auto-adaptive double thresholding (AADT)
Macronavigation: color information; optical glyphs with automatic glyph binarization
AADT compared with baseline and AAT: accuracy, precision, robustness, execution time
Glyphs evaluated on accuracy and execution time
2 / 35

## Slide 3
Reference: Section I. Introduction
Problem Statement
Indoor navigation is one of the most difficult activities for persons with visual impairment
Micronavigation: sensing the immediate environment for obstacles and hazards
Macronavigation: reaching remote destinations beyond the immediate environment
Users must confirm the place in front of them is the right destination
3 / 35

## Slide 4
Reference: Section I. Introduction
Limitations of Conventional Tools
White cane: detects obstacles at ~1,500 mm on average; micronavigation only
Guide dog: helps with both aspects of wayfinding
Guide dog: needs training; cost is prohibitive for most people
4 / 35

## Slide 5
Reference: Section I. Introduction & Section II. Micronavigation
Limitations of Electronic Travel Aids (ETA)
Laser/ultrasonic: poor environmental information; micronavigation only
Laser/ultrasonic: mapping the full scene needs several sensors, adding complexity
GPS: poor satellite coverage indoors significantly decreases accuracy
RFID: infrastructure-dependent; tags must be preinstalled by technicians
Combining many technologies can be complex, cumbersome and expensive
5 / 35

## Slide 6
Reference: Section I. Introduction & Section II
The Proposed Solution
Low-cost RGB-D cameras such as Microsoft Kinect
Two images: depth image and color image
Depth image: distance to the nearest physical surface, per pixel
Color image: recognizes printed markers at points of interest
One sensor perceives the whole scene; printed markers replace RFID
6 / 35

## Slide 7
Reference: Section III. System Architecture
INVys System Architecture
Obstacle detection: AADT finds the closest obstacle and its distance in mm
Glyph recognition: processes color images to find and classify glyphs
Feedback: decision module decides if feedback is needed
Feedback module delivers sound or voice
[ Figure 1 ]
Figure 1. INVys architecture consists of three subsystems.
7 / 35

## Slide 8
Reference: Section II. Micronavigation
Prior Approaches to Micronavigation
Laser (triangulation) and ultrasonic (time of flight) are common
Basic depth method: user height and width used to find farthest reachable point
Other methods split the depth image into areas processed separately
Other methods combine depth and color via image processing or computer vision
INVys: few areas for easy directions + depth-histogram analysis
8 / 35

## Slide 9
Reference: Section IV.A. Basic Requirement
Obstacle Detection Strategy
"Friendliness" defines the maturity of an avoidance system
Region in front divided into three paths: left, middle, right
Users only remember three directions
At 1,500 mm each subarea covers objects up to 549 mm wide
549 mm exceeds average shoulder breadth of Singaporeans and Indonesians
[ Figure 2 ]
Figure 2. Captured image in front of persons with visual impairment is divided into three regions.
9 / 35

## Slide 10
Reference: Section IV.B. Baseline Approach
Baseline Detection Method
Depth image 640 × 480 at 30 fps: more than 9 million depth samples
Image divided into 32 × 40 blocks; block averages computed
Blocks grouped into 5 × 3 regions; ten middle sorted values kept
Result: 15 distance values, one per region
10 / 35

## Slide 11
Reference: Section IV.C. Auto-Adaptive Thresholding (AAT)
AAT Overview
Initial version of AADT
Generates thresholds specific to each depth subarea
Three areas, each converted to a depth histogram
Finds the two closest peaks; applies Otsu thresholding between them
Otsu maximizes between-class variance (Eq. 1–2)
Separates the closest object from objects behind it
11 / 35

## Slide 12
Reference: Section IV.C. Auto-Adaptive Thresholding (AAT)
Limitations of AAT
Effective when the object is closer than 2,500 mm
Accuracy declines beyond 2,500 mm
Cannot separate object from the floor when the floor is detected beyond 2,500 mm
12 / 35

## Slide 13
Reference: Section IV.D. Auto-Adaptive Double Thresholding (AADT)
Introduction to AADT
Further development of AAT
Solves object-vs-floor confusion beyond 2,500 mm
AAT uses one threshold; AADT produces two
Double threshold generated automatically, varying per area
Differs from AAT in peak selection, thresholds and final distance
13 / 35

## Slide 14
Reference: Section IV.D.1–2
AADT Processing: Steps 1 and 2
Step 1: raw Kinect depth converted to 8-bit grayscale (Eq. 3)
Grayscale is used to visualize depth on screen
Step 2: image divided into left, middle and right areas
This step and later ones run at 2 Hz
Areas processed separately and simultaneously
14 / 35

## Slide 15
Reference: Section IV.D.3–4
AADT Processing: Steps 3 and 4
Step 3: downsampling uses one pixel per 2 × 2 block
Reduces data and speeds computing
Step 4: pixels categorized into 100 histogram groups
40 mm per group, covering 0 to 4,000 mm
15 / 35

## Slide 16
Reference: Section IV.D.5. Peak Detection and Selection
AADT Processing: Step 5
Local maximum in the histogram usually indicates an object
Contrast value computed per group (Eq. 4); parameter n filters noise
Criterion 1: contrast larger than 300
Criterion 2: local maxima more than four groups apart
Selected peak: closest to the Kinect (smallest group number)
16 / 35

## Slide 17
Reference: Section IV.D.6. Double Threshold Selection
AADT Processing: Step 6
Two thresholds (T1, T2) separate the closest peak from surrounding data
T1: first local minimum at a smaller distance than the peak
T2: first local minimum at a larger distance than the peak
Found via slopes; stop where gradient changes dramatically
Algorithm 1 gives T1; Algorithm 2 gives T2
Extra rule: frequency at threshold below half the peak frequency
17 / 35

## Slide 18
Reference: Section IV.D.7. Final Distance Calculation
AADT Processing: Step 7
Average of depth values between T1 and T2 (Eq. 5)
Output: three distance values in millimeters
One each for left, middle and right areas
18 / 35

## Slide 19
Reference: Section V. Glyph Recognition
Macronavigation via Optical Glyphs
Optical glyph: printed square grid with equally divided rows and columns
Cells black or white; first and last row/column all black
Adapted from augmented reality to convey signs, places and interest points
Based on Andrew Kirillov's method; enhanced binarization
Color camera 640 × 480 at 30 fps
Two steps: image processing, then glyph recognition
19 / 35

## Slide 20
Reference: Section V.A.1–3
Glyph Image Processing (Part 1)
Grayscale: ITU-BT.709 weights 0.2125 R, 0.7154 G, 0.072 B
Edge detection: max difference between neighbor pixels in four directions (Eq. 6)
Blob detection: threshold the edges image to binary
Connected component labelling groups pixels by connectivity
[ Figure 3 (a)–(e) ]
Figure 3 (a)–(e). Acquired RGB, grayscale, edges, binary and blob images.
20 / 35

## Slide 21
Reference: Section V.A.4–6
Glyph Image Processing (Part 2)
Rectangle detection: bounding box, center, then four corners
Lines between corners must be within the distortion limit (Eq. 7)
Glyph detection: brightness inside vs outside the rectangle
Black border surrounded by white gives a very high difference
Cropped glyph converted to binary with Otsu thresholding
[ Figure 3 (f)–(g) ]
Figure 3 (f)–(g). Detected glyph in grayscale and in binary.
21 / 35

## Slide 22
Reference: Section V.B. Recognition (Glyph Binarization)
Automatic Glyph Binarization
Glyph split into s × s cells, each converted to 0 or 1
Beyond 60% black: 0; beyond 60% white: 1
Kirillov's method needs glyph size set in advance
Automatic method tests sizes from 10 × 10 down to 5 × 5
Larger than 10 × 10 is rarely used
White data (1) starts from the second row/column (Algorithm 3)
[ Figure 3 (h)–(i) ]
Figure 3 (h)–(i). Glyph binarization process and its result.
22 / 35

## Slide 23
Reference: Section V.B. Recognition (Glyph Matching)
Glyph Matching
Binarized matrix compared with database matrix
Four conditions: ideal, rotated 90°, 180°, 270°
Done by rotating the matrix and comparing values
23 / 35

## Slide 24
Reference: Section VI.A. Hardware Configuration
Hardware Setup
Microsoft Kinect 360 as RGB-D camera
Battery pack powers the Kinect
Laptop/computer tablet runs the INVys software
Earphone delivers feedback
Kinect: 640 × 480 depth, 3,500 mm range, 57.5° horizontal, 43.5° vertical view
[ Figure 4 ]
Figure 4. INVys hardware parts worn by the user and the data flow between them.
24 / 35

## Slide 25
Reference: Section VI.B.1. Obstacle Detection
Micronavigation Experiment Design
Camera at 890 mm (average hip height, 50-year-old Indonesians)
Six objects: human, chair type 1, chair type 2, trash, electric fan, piles of cardboard
18 positions: six per depth image area
Estimated vs real distance in millimeters
Methods: baseline, AAT, AADT
[ Figure 5 (a)–(b) ]
Figure 5 (a)–(b). Blindfolded man conducting the experiment; the 18 object positions.
25 / 35

## Slide 26
Reference: Section VI.B.2. Glyph Recognition
Macronavigation Experiment Design
Five glyph patterns; two sizes: A (6 × 6 cm), B (11.5 × 11.5 cm)
Tested every 300 mm until no longer recognized
Normal: ideal, then rotated clockwise 90°, 180°, 270°
Tilted: 45° to left-back, right-back, top-back, bottom-back
Tilt matters because the camera moves with the user
[ Figure 6 (a)–(b) ]
Figure 6 (a)–(b). Glyph recognition experiment in normal and tilted conditions.
26 / 35

## Slide 27
Reference: Section VI.B. Performance Indicators
Evaluation Metrics
Accuracy: average distance error between estimate and truth (Eq. 8)
Precision: consistency over many trials, measured by CDF
Robustness: consistent accuracy along the camera's depth coverage
Execution time: speed in real-time conditions
Glyph tests: accuracy (% recognized) and execution time
27 / 35

## Slide 28
Reference: Section VI.C.1. Results (Accuracy)
Obstacle Accuracy Results
AADT smallest average error: 50.2 mm (SD 87.7 mm)
All algorithms worse when the floor was detected
AADT stayed below 100 mm in both floor conditions
Baseline and AAT errors were far higher
[ Figure 7 (a)–(b) ]
Figure 7 (a)–(b). Average error per algorithm; floor detected vs not detected.
28 / 35

## Slide 29
Reference: Section VI.C.1. Results (Precision)
Obstacle Precision Results
Normal error range for AADT: 0 to 137.9 mm
93.5% of AADT errors below 100 mm, over 108 trials
AAT: only 53.7% within 100 mm (CDF 0.537)
AADT is the most precise
[ Figure 8 ]
Figure 8. CDF of distance calculation errors over many trials.
29 / 35

## Slide 30
Reference: Section VI.C.1. Results (Robustness)
Obstacle Robustness Results
Baseline: acceptable to 2,000 mm, then errors too high
AAT: below 200 mm to 2,500 mm; over 600 mm at 3,500 mm
AADT: below 150 mm across the whole camera range
AADT error range across distances: only 103.3 mm
About 21.3 mm accuracy loss per 500 mm of distance
[ Figure 9 ]
Figure 9. Accuracy of each algorithm as obstacle distance increases.
30 / 35

## Slide 31
Reference: Section VI.C.1. Results (Execution Time)
Execution Time Results
Baseline: 7.41 ms (SD 1.19)
AAT: 7.05 ms (SD 1.22)
AADT: 9.50 ms (SD 3.61)
AADT slower, with only small differences
AADT better on accuracy, precision, robustness
[ Table I ]
Table I. Average execution time of baseline approach, AAT, and AADT.
31 / 35

## Slide 32
Reference: Section VI.C.2. Results (Distance)
Glyph Accuracy by Distance
Accuracy is inversely proportional to distance
Accuracy is proportional to glyph size
At 120: glyph A 0%; glyph B above 90% (units as stated in paper)
Glyph A drops significantly at 600 mm or beyond
Average 300–1,500 mm: glyph B 91%, glyph A 38.5%
Minimum practical size: 11.5 × 11.5 cm or larger
[ Figure 10 ]
Figure 10. Average accuracy of glyph A (6 × 6 cm) and glyph B (11.5 × 11.5 cm) per distance.
32 / 35

## Slide 33
Reference: Section VI.C.2. Results (Time)
Glyph Execution Time
Average: glyph A 82 ms; glyph B 68 ms
Fastest: glyph A 53 ms; glyph B 41 ms
Slowest: glyph A 138 ms; glyph B 90 ms
Glyph B recognized better and quicker; difference is minute
[ Table II ]
Table II. Average execution time of glyph recognition, glyph A vs glyph B.
33 / 35

## Slide 34
Reference: Section VI.C.2. Results (Tilt)
Impact of Glyph Tilting
Tilted glyph A: lower accuracy at most distances
Tilted glyph B: clearly lower between 1,200 and 1,800 mm
At 1,500 mm: non-tilted 100%, tilted only 30%
Tilt reduces overall accuracy more than non-tilted conditions
[ Figure 11 (a)–(b) ]
Figure 11 (a)–(b). Tilted vs non-tilted accuracy for glyph A (a) and glyph B (b).
34 / 35

## Slide 35
Reference: Section VII. Conclusion and Future Works
Conclusion & Future Scope
Depth camera for micronavigation; color camera for macronavigation
AADT outperformed others: accuracy 50.2 mm, precision, robustness
Only weakness: execution time, judged negligible by the authors
Glyph B: 91% average accuracy at 300–1,500 mm vs 38.5% for glyph A
Future: positioning system and path planning without markers
Goal: guide users step by step between places
35 / 35